## Slide 1: Dust products
Some options

## Slide 2: Polar Multi-sensor Aerosol product (PMAp)
Climate record 2007–2019 (PMAp CDR)
Output
AOD (GOME-2)
Aersool types and clouds (IASI, AVHRR)
Dust as non-operational product…
PMAp (dust-dominated total AOD contribution from other aerosol types than dust)
LEO
Aerosol types: ocean fine mode, ocean coarse mode, thick biomass burning, desert dust, volcanic ash/thick dust, volcanic ash with SO2, aerosol contaminated cloud, ash contaminated cloud, unclassified

## Slide 3: Polar Multi-sensor Aerosol product (PMAp)
Inputs:
GOME-2 Fundamental Data Record (FDR) Level 1C
IASI FDR Level-1C NRT
AVHRR Level 1B NRT

## Slide 4: Polar Multi-sensor Aerosol product (PMAp)
Algorithm:
cloud identification and correction using collocated AVHRR observations
discrimination between aerosols and clouds
preliminary classification of aerosols, including desert dust detection.
AODs also for partly cloudy footprints,
retrieval of estimated AOD using unpolarised GOME-2 reflectances and a Look-Up-Table
set of AOD estimates is retrieved for each candidate aerosol model.
find the best fit between the measured and modelled reflectances and Stokes fractions
best model (LUTs from 9 models), for each aerosol, aerosol type is set and final AOD from the AODs retrieved at the second step is selected
Validation:
AERONET

## Slide 5: Polar Multi-sensor Aerosol product (PMAp)
PMAp –> AODs @ 550nm
not possible to define the dust fraction (or AOD related to dust particles only) from a PMAp total AOD
Define the dust-dominated total AOD where the aerosol class is set to “desert dust” or “thick dust” for pixels which the assumed dominant aerosol type is dust
“total AOD” “dust-dominated total AOD”
WORKS but:
for subset of data/domain
against specially filtered AERONET data
better describing dust occurrence and variation
sensitive enough for high AOD cases involving dust
PMAp observations cannot be used to define DAOD global variation

## Slide 6: Thanos AOD retrieval (we need a nice name)
Inputs:
Temperature @10.8μm (MSG –> update σε MTG)
Land Surface Temperature (ERA5 –> update σε MTG1)
Humidity (ERA5)
Constant from MODTRAN4 (more model runs)
Cloud mask (MSG/MTG)

## Slide 7: Thanos AOD retrieval (we need a nice name)
Difficulties:
Discrimination of dust from clouds
Define/choose a rolling pristine sky
ERA5 latency 5 days for preliminary, 2-3 months for final
Validation:
AERONET
Sentinel-3?
Upgrades:
Automation
Machine learning